## Slide 1
Parking Assessment
Occupancy survey results by area
The corridor average hides the spread — and the areas under the most pressure are the ones with the least room next door
1
Surveyed area
Peak occupancy
Zones over
85% at peak
Spaces
removed
Displaced
(% of spaces removed)
Re-absorbed
(% of displaced)
Avg. stay
Kentron (Corridor 1 core)
138%
89%
408
81%
10%
2.2 h
Gai Avenue (Mega Mall)
123%
90%
132
99%
68%
2.0 h
Komitas Avenue
123%
81%
253
89%
0%
1.8 h
Garegin Nzhdeh
92%
61%
286
52%
30%
1.7 h
Shiraz / Hasratyan
75%
47%
439
42%
69%
1.6 h
Malatia-Sebastia
54%
27%
368
27%
97%
1.6 h
Pressure and absorptive capacity run in opposite directions
• Kentron and Komitas peak over capacity yet re-absorb only 10% and 0% nearby; Malatia-Sebastia peaks at 54% and re-absorbs 97% — so the package is applied by zone, not uniformly.
Peak occupancy = distinct vehicles over the busiest hour ÷ spaces; above 100% means more distinct vehicles than spaces used the kerb in that hour. It sums each zone's own peak hour, so zones busiest at different times are added together. Displaced (% of spaces removed) instead counts one shared clock hour — a stricter basis, so the two columns are not directly comparable; on the single-hour basis Kentron reads 89% and Komitas 83%. Surveyed areas only, not corridor-wide. Source: field occupancy survey, 29 May – 3 June 2026.