## Slide 1
Parking Assessment
Parking Assessment
1
Our goal
• Analyse the existing parking system context along the priority corridors and in Yerevan as a whole.
• Assess the impacts of the conceptual corridor designs on parking supply.
• Evaluate the potential for parking displacement within the defined influence area.
• Identify mitigation options and parking management measures that support corridor implementation.
What we did
• Parking Supply Survey — desk inventory from 360° video, satellite and Yandex imagery, with ~15% cross-checked physically in the field.
• Parking Occupancy Survey — six representative areas, hourly license-plate sweeps, 07:00–24:00.
• Off-street context — major facilities on the corridors catalogued to test their potential to absorb displaced demand.
• All survey data published and explorable at http://yerevan-parking.vercel.app
Field occupancy survey areas

## Slide 2
Parking Assessment
Parking Supply Survey
Across the corridors and 100 m buffer
2
15,883
Total spaces inventoried
8,848
On-street, across 728 segments
6,991
On the corridors themselves
7,035
Off-street, across 266 facilities
On-corridor on-street supply by regulatory zone (6,991 spaces)
Free / unregulated 6,144 (87.7%)
Zone B (blue) – paid 534 (7.6%)
Zone A (red) – paid 246 (3.5%)
Taxi 67 (1.0%)
88% of corridor parking is free of charge — and barely organized
• Only 20% has signage and 12% has markings. Zone A is concentrated in Kentron (Nalbandyan 83, Abovyan 46, Amiryan 43); Zone B is almost entirely Komitas Avenue (522 of 534).

## Slide 3
Parking Assessment
Parking Occupancy Survey
6 areas | hourly license-plate sweeps | 29 May - 3 June 2026 | 07:00–24:00
3
Peak occupancy by surveyed area
Peak occupancy = the total number of distinct vehicles recorded over the busiest hour ÷ the number of spaces (capacity-weighted). It is an hour-long count rather than a single snapshot, so a reading above 100% means more distinct vehicles than spaces used the kerb within that hour — the spaces turned over.
93%
Peak occupancy, capacity-weighted
1.8h
Average length of stay
5–11
Vehicles per space per day
63%
Of stays are one hour or less
How long vehicles stay

## Slide 4
Parking Assessment
Occupancy survey results by area
The corridor average hides the spread — and the areas under the most pressure are the ones with the least room next door
4
Surveyed area
Peak occupancy
Zones over
85% at peak
Spaces
removed
Displaced
(peak hour)
Re-absorbed on
nearby streets
Avg. stay
Kentron (Corridor 1 core)
138%
89%
310
250
14%
2.2 h
Gai Avenue (Mega Mall)
123%
90%
132
131
68%
2.0 h
Komitas Avenue
123%
81%
108
93
0%
1.8 h
Garegin Nzhdeh
92%
61%
286
150
30%
1.7 h
Shiraz / Hasratyan
75%
47%
439
185
69%
1.6 h
Malatia-Sebastia
54%
27%
368
99
97%
1.6 h
Pressure and absorptive capacity run in opposite directions
• Kentron and Komitas peak over capacity yet re-absorb only 14% and 0% nearby; Malatia-Sebastia peaks at 54% and re-absorbs 97% — so the package is applied by zone, not uniformly.
Peak occupancy = distinct vehicles recorded over the busiest hour ÷ the number of spaces; above 100% means more distinct vehicles than spaces used the kerb within that hour. Spaces removed and displaced demand are for the surveyed areas only, not corridor-wide. Source: field occupancy survey, 29 May – 3 June 2026.

## Slide 5
Parking Assessment
Occupancy Survey Locations
5
Kentron (Corridor 1 core)
138% peak
Gai Avenue (Mega Mall)
123% peak
Komitas Avenue
123% peak
Garegin Nzhdeh
92% peak
Shiraz / Hasratyan
75% peak
Malatia-Sebastia
54% peak
Measured occupancy
≤85% — within capacity
86–100% — at capacity
>100% — over capacity
Off-street yard (dashed)

## Slide 6
Parking Assessment
Design Impact & Displacement Assessment
The conceptual cross-section removes 85% of on-corridor parking
6
CORRIDOR-WIDE · impact of the conceptual design
Corridor 1: 1,494 · Corridor 2: 3,395
6,991
On-street, on the corridors
4,875
On-street spaces removed
70%
Of on-corridor parking
2,116
Retained or re-established
SIX SURVEYED AREAS ONLY · measured displacement
A demand overlay — not a re-survey of the full corridor
55%
Displaced vs. removed
43%
Absorbed on-street
92%
Capacity behind gates
Open and manage the yards BEFORE removing kerb: nearby streets absorb only 43% (14% in Kentron, 0% in Komitas). Re-absorption reaches ~100% only via off-street, and 92% of that is gated residential yards.
Displaced demand = distinct vehicles in the removed zones at each area's single busiest hour, summed across the six areas.
The 55% is the displaced demand set against the spaces removed in the same six areas (908 vehicles ÷ 1,643 spaces): the kerb is not full at the moment, so fewer vehicles need re-homing than spaces are lost. Corridor-wide removal and retention figures follow the current conceptual design and will be updated once that design is finalized.

## Slide 7
Parking Assessment
Mitigation Measures by Sensitivity Zones
No single measure resolves displacement - the package is applied selectively, by measured zone sensitivity
7
HIGH SENSITIVITY
MEDIUM SENSITIVITY
LOWER SENSITIVITY
High
Medium
Lower
Exception — Gai Avenue (Mega Mall)
• Kerb parking stays for now; revisit as the area changes - mall parking or the planned BRT.
Extend paid zones LEAD
Open residential yards
Delivery bays
Resident permits
Visitor caps
Extend paid zones
Delivery bays
Organise free parking
Open residential yards

## Slide 8
Parking Assessment
Further studies and considerations
Parking is a citywide system and cannot be sustainably managed at corridor level alone
8
This component is scoped to the BRT corridors and their immediate influence area. The measures proposed here should therefore be understood as the first stage of a broader, citywide reform.
Extend the approach citywide
• Extend the parking study beyond the corridor buffer to a citywide scale.
• Apply focused demand assessments at selected high-pressure locations, rather than corridor-wide observational surveys.
• Progressively expand the red-line zonal system into neighbourhoods currently outside it.
Supporting studies
• Residential yard opening.
• Legal basis of the resident permit scheme.
Priority: who administers residential-yard opening
• The yards carry ~92% of the absorptive capacity that makes re-absorption work, yet no body currently owns the task. Who should lead it, and under what organisational and legal arrangement, warrants a dedicated study before any roll-out.