## Slide 1
Parking Assessment
Parking: what has changed since April
The demand side is now measured, not inferred — six representative areas surveyed 29 May – 3 June 2026
2
93%
Peak occupancy, capacity-weighted
63%
Of vehicles stay one hour or less
55%
Displaced demand vs. spaces removed
5–11
Vehicles per space per day (turnover)
April 2026 — inferred
• Occupancy survey descoped on proportionality grounds
• Displacement argued from European BHLS precedent — Nantes, Metz, Rouen, Eindhoven, Helsingborg
• Re-absorption asserted, not quantified
June 2026 — measured in Yerevan
• 908 cars displaced at the peak hour against 1,643 spaces removed
• The European finding is now confirmed by local measurement
• Re-absorption quantified — and its precondition exposed
Six areas: Kentron, Komitas, Gai Avenue, Garegin Nzhdeh, Shiraz/Hasratyan, Malatia-Sebastia. Hourly licence-plate sweeps, 07:00–24:00, on four ordinary mid-week working days.

## Slide 2
Parking Assessment
Approach: how the evidence was built
A desk-based supply inventory, completed by a targeted field occupancy survey
2
1 · Desk-based supply inventory
• 994 geo-referenced features — 728 on-street segments and 266 off-street facilities
• Built from 360° street video (yerevan.omni7.app), satellite and street-level imagery
• Parallel capacity = length ÷ 7.5 m; angled bays counted individually
• ~15% of spaces independently cross-checked, plus on-the-spot field visits
• Published live at yerevan-parking.vercel.app
2 · Field occupancy survey (targeted)
• Six representative areas spanning the corridor sensitivity range
• Hourly licence-plate sweeps, 07:00–24:00, four ordinary working days
• Records time, zone, plate, vehicle type, kerb location, parking method and legality
• Yields occupancy, duration of stay and turnover directly
• Areas spread across separate days, so a one-off disruption shows as a local outlier
The ToR is met in substance, not departed from
• The occupancy component, initially descoped on proportionality grounds, is now satisfied in representative form — the deliverable meets the intent of the ToR rather than departing from it.

## Slide 3
Parking Assessment
Supply baseline: 15,897 spaces surveyed
Three bus priority corridors (34.6 km) and their 100-metre influence area
2
15,897
Total spaces surveyed
8,862
On-street spaces (728 segments)
7,035
Off-street spaces (266 facilities)
7,005
On-street, on the corridors themselves
On-corridor on-street supply by regulatory zone (7,005 spaces)
Free / unregulated 6,144 (87.7%)
Zone B (blue) – paid 534 (7.6%)
Zone A (red) – paid 260 (3.7%)
Taxi 67 (1.0%)
88% of corridor parking is free — and barely organised
• Only 20% of on-corridor spaces have signage and only 12% have markings. The supply is not just cheap, it is unstructured — which is why organising it is a measure in its own right.
Totals corrected June 2026 (off-street 7,479 → 7,035; total 16,341 → 15,897). On-street and cross-street figures are unchanged.

## Slide 4
Parking Assessment
Demand: the kerb is saturated at the peak
Capacity-weighted peak occupancy of 93%, with 69% of zones above the 85% efficiency threshold
2
Peak occupancy by surveyed area
85% threshold
Kentron
138%
Komitas
123%
Gai Avenue (Mega Mall)
123%
Garegin Nzhdeh
92%
Shiraz / Hasratyan
75%
Malatia-Sebastia
54%
93%
Peak occupancy, capacity-weighted
69%
Of zones above the 85% threshold
116
Zones over legal capacity at the peak
Occupancy above 100% is chronic overflow — more vehicles present than legal striped capacity. Only ~0.2% of vehicles were flagged as illegally parked: the issue is saturation and tolerated informality, not overt illegality.

## Slide 5
Parking Assessment
Demand: a short-stay, high-turnover kerb
Parking is dominated by short visits; genuine all-day storage is a small tail
2
63%
Stay one hour or less
77%
Stay two hours or less
1.8 h
Average stay
5–11
Vehicles per space per day
Visitors & customers — ~63%
The dominant group: short retail and errand access. This is the demand the kerb actually serves.
Commuters & workers — ~6%
A small all-day tail. Better addressed as a BRT mode-shift opportunity than as a fining target.
Residents — ~7% overnight
Under-counted by a daytime window (07:00–24:00). To be protected by the permit scheme, not squeezed.
Implication: visitor caps address a problem the data does not show. Turnover is already high, so pricing — not maximum-stay enforcement — is the binding lever.

## Slide 6
Parking Assessment
Impact: 85% of on-corridor parking is removed
Inherent to the central-median cross-section — a design consequence, not an incidental one
2
5,953
On-street spaces removed
1,052
Spaces retained or re-established
85%
Of the on-corridor supply removed
Corridor 1 — 11.66 km
1,836 spaces removed
Bagratunyats (south) to Kentron; carries the Zone A core.
Corridor 2 — 19.19 km
3,310 spaces removed
Nor Nork (east) to Davtashen; the largest single loss.
Corridor 3 — 3.81 km
807 spaces removed
Sebastia/Malatia; entirely residential off-street context.
Cross-section: 2 × 3.5 m bus lanes, 2 × 3.0 m mixed traffic per direction, 0.5 m separators, cycle lanes and 2.50 m sidewalks — leaving no carriageway width for parking. Consistent with the Mott MacDonald (2022) strategy and the Yerevan Sustainable Urban Transport Strategy.

## Slide 7
Parking Assessment
Displacement: measured, not inferred
Peak displaced demand equals only 55% of the spaces removed — the European finding, now measured in Yerevan
2
1,643
Spaces removed in the surveyed areas
908
Cars actually displaced at the peak hour
55%
Displaced demand as a share of supply removed
Share of displaced demand absorbed on nearby streets
Kentron
14%
Komitas
0%
Gai Avenue (Mega Mall)
68%
Garegin Nzhdeh
30%
Shiraz / Hasratyan
69%
Malatia-Sebastia
97%
Why this matters
• Not every removed space needs replacing one-for-one
• Some users shift mode, retime, or were parked informally
• But on-street alone absorbs just 43% — the rest must come from off-street
Surveyed areas only — a subset of the corridor-wide 5,953 removals. Measured at the peak hour, the binding case.

## Slide 8
Parking Assessment
The catch: re-absorption depends on opening gated yards
About 92% of the absorptive capacity is gated residential yards, counted at gross capacity as if already open
2
~100%
Aggregate re-absorption — best case
43%
Absorbed by surviving on-street capacity
92%
Of absorptive capacity sits behind gates
Observed occupancy in the six surveyed off-street facilities (427 spaces)
Area
Facility
Spaces
Avg.
Peak
Gai Avenue (Mega Mall)
Palace lot
32
115%
194%
Kentron
Nalbandyan yard
60
81%
142%
Komitas
Komitas City lot
123
56%
101%
Malatia-Sebastia
Sebastia yard
101
32%
77%
Shiraz / Hasratyan
Shiraz off-street
71
37%
59%
Garegin Nzhdeh
GN off-street
40
22%
45%
All six — 427 spaces, ~52% full on average across the day
Why this is load-bearing
• Three of the six are already at or over capacity at the peak
• Those facilities carry their own demand — excluded from the absorptive count
• The capacity that closes the gap is still behind gates
• So: open and manage the yards BEFORE removing kerb
Kentron is ~86% yard-dependent, Komitas ~100%. Opening yards is largely untested in post-Soviet courtyards — ownership, consent and revenue-sharing need a dedicated study.

## Slide 9
Parking Assessment
What the measured evidence changed
Each mitigation measure re-tested against the field survey — two were materially revised
2
Extend paid zones
CONFIRMED — LEAD
About 90% of the kerb is unpriced. Roll the red/blue-line regime onto side streets within 100 m, with ANPR enforcement.
Organise free parking
CONFIRMED — WIDEN
88% of corridor parking is unmarked and 24.5% sits off the carriageway. Widen beyond outer zones: Komitas (35% informal), Kentron (60% angled).
Open residential yards
NOW A PRECONDITION
Carries about 92% of the absorptive capacity. Re-absorption is conditional on opening these yards — no longer an optional outer-zone pilot.
Delivery spaces
CONFIRMED — RE-SIZE
Size loading bays to the measured freight pockets — truck share 12.6% in Malatia-Sebastia and 8.0% in Shiraz against 4.9% citywide — not uniformly.
Resident permits
KEEP — BUT PRICE IT
Tbilisi is a cautionary case, not a model: two free vehicles per apartment produced exactly the long-stay pattern to avoid. Price or cap from the outset.
Visitor caps
RE-SCOPE
The data contradicts the premise: 63% of vehicles already stay an hour or less and all-day parking is ~6%. Demote to a targeted contingency; lead with pricing.
Park & ride
FUTURE STUDY
The daytime fleet is overwhelmingly short-stay, so P&R is not the binding lever now. Retain as a strategic study item for the BRT terminals.
Also flagged
• Phase out the flat annual permit — it removes the marginal cost of dwell time and so works against the turnover the data shows is the binding lever.
• A candidate idea, not yet a measure: substantiate with PCS permit-uptake and tariff data first.
The corridor itself remains the primary mitigation: faster, more reliable public transport reduces the number of trips that need to park at all. Every measure above is complementary to that structural shift.

## Slide 10
Parking Assessment
Mitigation packages by sensitivity zone
Recalibrated by the survey: Komitas moves up to high sensitivity; Gai Avenue is handled as an exception
2
HIGH SENSITIVITY
Kentron CBD · 138% peak · 14% absorbed
Komitas · 123% peak · 0% absorbed
— moved up from medium by the survey
• Extend paid zones — lead
• Open residential yards — precondition
• Delivery spaces
• Resident permits
• Visitor caps — contingency only
MEDIUM SENSITIVITY
Arshakunyats · Kievyan
Substantial pressure, but more nearby capacity than the core
— orderly redistribution
• Extend paid zones
• Delivery spaces
• Park & ride where relevant
LOWER SENSITIVITY
Shiraz 75% · Malatia-Sebastia 54% peak
Bagratunyats, Sebastia, Raffi, Nor Nork
— structure before pricing
• Organise free parking
• Park & ride
• Open residential yards
Exception — Gai Avenue (Mega Mall)
• 123% peak. Even filling every nearby yard leaves demand unaccommodated (89% best case) — so the kerb parking stays for now, to be revisited as the area changes.

## Slide 11
Parking Assessment
Conclusions and next steps
The parking case is now evidence-based end to end — with one load-bearing condition
2
Conclusions
• Parking loss is substantial and inherent to the design — about 85% of on-corridor supply (5,953 spaces).
• The demand side is now measured, not inferred: 93% peak occupancy, short-stay and high-turnover.
• Displaced demand is only 55% of the spaces removed — the European finding, confirmed locally.
• Re-absorption approaching 100% is achievable but conditional on opening gated yards (92% of capacity).
• Mitigation must be layered, and must precede kerb removal rather than follow it.
Next steps
• A dedicated residential-yard opening study: ownership, consent thresholds, revenue-sharing, enforcement.
• Extend the supply inventory citywide, beyond the corridor buffer.
• Progressively expand the red-line zonal system into the influence-area side streets.
• Park & ride feasibility; resident-permit legal basis; willingness-to-pay to calibrate tariffs.
• Monitor side-street occupancy after commissioning and adapt pricing and enforcement.
Sequencing is the decision that matters
• Removing kerb capacity ahead of opening the yards would strand the displaced demand the survey measures. Mitigation before removal is load-bearing, not advisory.
Full interactive results: yerevan-parking.vercel.app · Detail in Output 8 (Parking Surveys and Analysis) and Output 10 (Parking Analysis).